Accelerometers Production Technological Process Decomposition Parameters Model

Nevlydov Igor, Yevsieiev Vladyslav, Miliutina Svitlana, Bortnikova Viktoriia

Department of Technology and Automation of Radio Electronic and Computing Devices Production, Kharkiv National University of Radioelectronics, UKRAINE, Kharkiv, Nauki Ave, 14, E-mail: viktoriia.bortnikova@nure.ua, vladyslav.yevsieiev@nure.ua

Abstract - In this paper the accelerometer production technological process parameters decomposition model is described.

Keywords - Accelerometer, MEMS, technological process, decomposition.

I. Introduction

Current trends in the micro-electromechanical systems (MEMS) production require new approaches to improve the computer-aided design, which should satisfy the growing need for the development of effective technological processes (TP). In such conditions, existing approaches to the accelerometers production TP design automation should take into account the Industry 4.0 standards. However, the existing CAD systems do not allow to consider this and only automate one part of the TP [1]. The result is that today the task of accelerometers TP computer-aided design new methods developing is relevant.

To solve this problem it is necessary to develop a new basic parameters decomposition model that describe their relationships within the TP, which will allow to develop methods for computer-aided design accelerometers from the beginning to the end of the TP.

II. Accelerometers Production Technological Process Decomposition Parameters Model

Let  – preform for accelerometer production, which is a substrate comprising the basic parameters (the substrate material, substrate thickness, substrate size, crystallographic orientation).

Therefore, basing on the TP theory we can present that the accelerometers production is a sequence that includes a plurality of production stages  (substrate type selection, substrate preparation and so on), which are the technical process enlarged part: they are almost independent, are characterized by a logical completeness, spatial or temporal isolation. So, , where , for this research let’s limit  – the main famous stages, presented on fig.1.

The whole accelerometer production technological process may be represented as a process of transition from the preform  to the ready accelerometer  by performing a set of some stages sequences .

In the TP implementation of the preform qualitative and quantitative characteristics are changed. The result is that in general each stage may be represented as an action sequence over for end-product  getting.

Fig.1 Accelerometers Production Main Stages Sequence

So, we can write an expression:

(1)

Taking into account, that stages  represent a sequence, we can expand expression 1 in such way:

(2)

So, a preform  represents a plurality of consecutive preform changes , where  is an identifier of belonging to n stage .

In turn, each stage  is divided into a number of technological operations , that represent TP complete part, performed at one workplace.

Each operation  is one of the methods, used for one or another operation execution (e.g., «flip-chip» method, «anisotropic etching» method). Each stage  is characterized by a different number of operations , which is determined by this stage , depending on the parameters (sensitivity, measured acceleration range etc.), which should have a ready accelerometer .

Then each stage  contains a number of operations  to be performed in order to proceed to and represents the set of sequences to be performed for the accelerometer .

Let’s introduce the concept as an ordered sequence of each stage . So. We can represent  as a plurality of interrelated operations sequence , where  is an identifier that shows operations belong to a certain stage, and  – is a operation serial number at the stage . Plurality  is an operations sequence, that are necessary and sufficient to be done to perform next stage .

Based on the above accelerometer production technological process presented in (2) can be represented in next way:

(3)

However, it is worth considering that in the TP construction (as shown in Fig. 1), there are stages , which do not change the preform  geometrical parameters, such as «substrate selection» stage (the definition of the material, size and substrate crystallographic orientation) and «control» stage, which are connected with the conduct of control after a certain stage (obtained sensor control, crystallography control, connections control, output control). Then, the stages , which will affect the geometric shapes, sizes and physicochemical properties of the preform  we’ll call the main stages and denote them , and those operations that do not affect the change of the preform  geometric dimensions and ensure the uninterrupted flow of the main stages , we’ll denote and call secondary stages.

Existing TP analyses [2,3] showed, that the first stage  of accelerometer production technological process always is a «substrate selection», and the last stage is always a «output control» and both these stages do not affect the geometric dimensions change, then:

, где , 		(4)

where  – the first stage of accelerometer production TP «substrate selection»;  – an initial preform (substrate) before stage ;  – a preform after stage .

A preform  is an initial preform (substrate), and a preform  is a next preform after stage . A preform  after stage  is done has the same geometrical and physical properties as the preform , because stage  doesn’t change its geometrical and physical properties, so, they are equal – . Therefore, in this research we assume that the presentation of the preform  which is obtained after stage, has an identifier  that indicates that its geometry is not changed.

It should be noted that at the stages  which modify the geometrical and physical parameters of the preform, . It can be concluded that the TP is an ordered sequence of transformations stages and  of the original preform to achieve ready accelerometer .

Based on the above and expressions 2-4 let’s write a  preform  changing stages sequence at an intermediate stage , depending on the type of process:

, (5)

Considering the expression 5 it can be concluded that if the stage is a stage  that , and vice versa if , so, .

On the basis of the proposed inequality it can be justified the presence of a stage  in a branch the TP construction. Stage  does not affect the  geometrical and physical parameters, but it is an integral part of the TP. This justification will introduce and take into account control stages in the transition points of the graph and avoid getting the wrong accelerometer.

Theorem 1: About the stages existence

The Theorem 1proof:

Let the stage does not exist, then there is always, and accelerometer production technological process can be written in such way:

However, if , then the entire the accelerometer production TP can be presented in next way:

As a result the TP on any part can be equal to zero, which makes it impossible to design the TP, and therefore rejects the assumption of the absence of stage .	Based on the foregoing, the accelerometer production technological process can be represented as a graph, where the vertices are the iterations carried out on the preform , and the edges are the ordered sequence of stages  and .

Then, the technological process sequence at stages 1-2 may be considered such that from the initial preform  in a specific order of application stages  and  we’ll obtain a preform , wherein the stage  is a stage that does not change the preform  geometric dimensions, then:

.	 (6)

This sequence should be presented as a graph, which has a closed cycle of variations for each stage .

Based on Theorem 1, on the stage , there are such options:

- if , then, there is no need to perform the stage  whereby ;

- if , then, there is a need to execute stage .

At the stage  a preform  must acquire all the necessary parameters inherent , so, preform  and the stage is performed until .

On Fig. 2 there is a graph reflecting stages  and  (in accordance with Fig. 1 – TP Stages 1 and 2) and the relationship with the state of the preform after each stage .

Fig.2 Accelerometer Production Technological Process at the Stages  and Graph

Fig. 2 designates the condition, which is necessary to perform the next step :

:« conditions value».

Settling on Theorem 1 let’s prove that there are operations  that lead to changes in the preform  geometric parameters and belong to the stages - and operations  that do not change the  geometric parameters belong to the stages  – .

So, the technological process shown in the expression 3 can be written as:

(7)

Then, based on the fig. 2 and expressions 6-7, for this research it must be considered an integral part of the TP as a transition, which is a part of a technological operation . Each operation includes a different number of transitions .

The transition should be understood in next way: for any operation  there is a transition , which is a completed operation  part, that is performed on one or more surfaces of the preform  by one or more tools working simultaneously without altering or automatic changing the working equipment modes.

For each operation  there is a main transition , that affects the preform  geometry change, and for each operation , there is a secondary transition  – a transition that does not cause changes in the preform  geometry, but it is necessary for main transition execution .

Thus, the deformation of the preform  occurs during the main  and secondary  operations execution, as well as main  and secondary  transitions.

In production conditions in any the TP we can identify options, and for each operation  and determine the interaction of various factors: accelerometer and sensor design, chassis design, machining accuracy and crystallography, the physicochemical properties of the accelerometer, the material costs of the operation.

Then define the factors in the operation  as  input parameters (characteristics of the initial preform  the and the preform , before to i-th operation  execution), the output  (the preform  characteristics after i-th operation execution ) and  variable technological parameters of the main  and secondary  transfer for i-th  operation and  execution respectively, i.e. parameters of any transition  and .

Then parameters , , , determine interaction  factors for any operation  and , they are interlinked, they have complex interactions and trey are combined in sets. Thus, any operation  and  can be represented as a system of interaction between the input  variable parameters  and the output parameters  of the operation .

The value of each parameter is within a certain range specified by the physical nature of this parameter or the TP requirements, so a constraints group associated with the parameters variation range, can be represented in the form of inequalities (8).

|  | (8) |
| --- | --- |

Each of the parameter sets, ,  is characterized by a set of these parameters allowable values. Let’s denote each element of sets , ,  as , , , and define these sets in such way (9).

|  | (9) |
| --- | --- |

Expression (9) shows, each element of sets , ,  is an subset , , , its elements are sets of limited values (min и max) within the values scope of this parameter.

The input parameters  for each operation  are those parameters that are obtained after each operation , and output parameters  are those parameters that are obtained after the operation  and are necessary to execute the operation . Each operation  contains a sequence of transitions , and transitions  contain variables .

Let’s represent the above in the form of interconnection that is shown in Fig. 4.

Fig.4 Parameters , ,  and transitions interconnection for each operation

However, options are not confined only to operations , but also for all the stages  there are input  and output parameters `. These parameters will have an identifier  and they are necessary in order to be able to evaluate and verify matching the preform  parameters after each stage . So, we can represent (7) in such way (10).

|  | (10) |
| --- | --- |

In (10)  represents initial parameters inherent the preform . The output parameters  obtained after the operation  must conform to a predetermined range of input parameters  for the operation . Then and only then we can assume that the TP should be consistently developed in accordance with the sequence and does not have significant deviations in terms of the set allowable range of parameter values.

Expression (10) represents an ideal accelerometer production TP, when output  and initial  parameters meet prescribed allowable range of values.

In order to take into account all the existing in real TP options let’s write these particular cases, which are presented below.

The first option, when the output parameters  obtained after an operation, correspond to the input parameters  for following operation :

In this case, we can proceed to the next operation: .

The second variant, when the output parameters  are less than the maximum allowable values for the input parameters :

In this case, you must return the preform  to the previous stage  and modify it until the output parameters  do not match the input parameters .

The third variant, when the output parameters  are smaller than the minimum allowable values for the input parameters :

In this case, the preform  can’t be modified in the previous stage  and represents a defective product. However, the preform  may be used in another TP where it will meet the specified parameters ().

Thus, the output parameters  do not always correspond to specify the correct values of the input parameters , and therefore special cases two and three may exist, and that should prove.

References

[1]. I. Sh. Nevlyudov, V.V. Yevsieiev, V.O. Bortnikova, Ya.O. Zamerets, “Microelectromechanical systems modern computer-aided design analysis,” Bulletin of the National Technical University "KhPI", Kharkiv, 2012, №66(972), pp.67-73.

[2] I. Sh. Nevlyudov, V.V. Yevsieiev, V.O. Bortnikova, “Accelerometers production existing technologies analysis based on microelectromechanical systems technology,”  XIV International Scientific Conference "Physical processes and fields of technical and biological objects,” Kremenchug, 2015, pp. 30-31.

[3] V.M. Teslyuk, “ Models and Information Technologies of microelectromechanical systems synthesis,” Lviv, 2008, 192 p.

III. Conclusion

In paper accelerometers production technological process decomposition parameters model is proposed. It allows to simplify technological process design and avoid the creation of "false" paths in the build tree. This is implemented due to the each TP parameter decomposition.

The model takes into account not only the main stages, operations and transitions, but also the concept of an intermediate and auxiliary control. This will enable the implementation of control parameters in operations  between stages . Thus, it will be possible to increase accelerometers production quality and reduce the percentage of defective products at finish. The model allows to identify defective products in TP building process and to modify their occurrence in the early stages. However, it will increase TP design time, but will significantly improve the quality and cost-effectiveness by monitoring the "weak" places in accelerometers production, thus providing a high competitive ability and increasing production economic characteristics.

# Text boxes

Substrate selection

Substrate preparation

Sensor getting

Sensor control

Crystallography

Crystallography control

Crystal installation to corps

Pins connection with the crystal

Connections control

Encapsulation

Output control